## Slide 1
CN0566 + PlutoSDR Four-Channel QPSK-OFDM Platform
Vivaldi TX • CN0566 phased receive array • Raspberry Pi 4 realtime audio / performance testing
stable_1m: 1 MSPS • FFT 256 • CP 32 • QPSK • 4 logical streams
Transmit software path on Raspberry Pi 4
RF / analog path
Receive + playback / performance path
4 WAV files
sample_1…4.wav
IMA-ADPCM
16 kHz mono
Packets
stream_id + CRC
FEC
rate 1/2
QPSK
mapper
OFDM
IFFT + CP
TX chunk
1 s buffer
Pluto TX2A
2.2 GHz IF
CN0566 TX_IN
upconvert
TX_OUT_2
Vivaldi
RF path
/ reflector
CN0566 array
RX2 path
Pluto RX2A
I/Q samples
OFDM sync
preamble
FFT + pilots
channel EQ
QPSK
soft bits
FEC + CRC
packet check
Stream
demux
Selected-channel
ADPCM decode
ALSA speaker
listen 1,3 / all
Recordings
+ metrics
Plots
constellation/PSD
Control and configuration plane
config.env
TX_GAIN / RX_GAIN
OFDM_PROFILE / LISTEN
pyadi-iio + libiio
URIs: ip:localhost
ip:192.168.2.1
CN0566 control
ADF4159 LO 12.4 GHz
ADAR1000 gain/phase
Pluto AD9361
TX=[1], RX=[1]
manual gains
Performance runs
timestamp folders
REPORT.txt + plots
Realtime safeguards
host_drop / tx_starve
PLL lock / EVM / BER
Key workflow concept
One RF waveform carries four logical audio streams.
The receiver can decode only the selected stream(s) for realtime playback, or decode all streams for performance tests.
Performance script captures hardware I/Q, analyzes offline, and writes timestamped folders containing waveform, eye, constellation, PSD, CSV metrics, and REPORT.txt.
Do not interpret tone FFT level as OFDM SNR. Use frame rate, host_drop, tx_starve, EVM, BER, and sequence gaps for realtime health.
Legend:
software
SDR
CN0566 / RF
RX/audio
metrics
Generated diagram for the current CN0566_OFDM_4CH_RPi4 selected-playback platform.